## Slide 1
Untitled Diagram.png
Bo Heyse Karina Paz Matt Healea
E2.10 – 3D Markerless Motion Capture System For Active Shooter Response Training
The System
Sponsored by the Texas State University ALERRT Center
Purpose
Acknowledgements
Approach
Battery Life – 13.82 Hours
Hardware
Inertial Measurement Unit (IMU) – Collect analog data
Microprocessor – Convert to digital and process data
Micro SD – Locally store data
Bluetooth Module – Create local area network among devices and transfer data upon completion of recording
Software
Process digital data
Visualization model
Advanced Heading and Reference System (AHRS),
Kalman Filter – To smooth the digital data
Results
What?
Virtualize Texas State ALERRT Center’s active shooter training scenarios
Why?
Allow smaller municipalities to have access to the training
How?
Build a wireless sensor-based system focused on collecting motion data at key points on a first responder
      ALERRT Center:
      Dr. Hunter Martaindale (Director of Research)
      Mr. Coby Briehn (Program Manager)
      Texas State University:
      Dr. Stan McClellan (Faculty advisor)
Background
The current industry standard for motion capture is a marker system that requires a 360-degree field of view, the wearer to be covered in restrictive equipment, and several high-resolution cameras.
Our system:
Is minimally invasive and does not require excessive equipment
Operates in dynamic environments
Low cost which will greatly enhance the availability of training for municipalities
Detailed Functionality
Ideal Sample Rate – 40 Hz
Project Goals
  Record motion and orientation of the body, gun, and head of the responder
  Non-intrusive design/integration with ALERRT Center equipment
  2-hour battery life – minimum
  Scalable design
  Simple and intuitive user interface
  Virtualize the motion of the body, head, and gun
Storage Capacity – 8.64 MB
Sensor System
User System
Admin System
A 40 Hz Sampling Rate Minimizes Angular Deviation